#### MQ – 135 Air Quality Sensor
The air quality sensor is also a MQ-135 sensor for detecting venomous gases that are present in the air in homes and offices. The gas sensor layer of the sensor unit is made up of tin dioxide (SnO2); it has lower conductivity compare to clean hair and due to air pollution the conductivity is increases. The air quality sensor detects ammonia, nitrogen oxide, smoke, CO2 and other harmful gases. The air quality sensor has a small potentiometer that permits the adjustment of the load resistance of the sensor circuit. The 5V power supply is used for air quality quality sensor.

The air quality sensor is a signal output indicator instruction. It has two outputs: analog output and TTL output. The TTL output is low signal light which can be accessed through the IO ports on the Microcontroller. The analog output is an concentration, i.e. increasing voltage is directly proportional to increasing concentration. This sensor has a long life and reliable stability as well.
#### Applications Of MQ 135 Gas Sensor
The following are the applications of the MQ 135 gas sensor:
- Air quality monitor
- Detection of harmful gases
- Domestic air pollution detection
- Industrial pollution detection
- Portable air pollution detection
#### Characteristics Of MQ 135
- Good sensitivity to harmful gases in wide range.
- It has long life and low cost.
- Possesses high sensitivity to ammonia, benzene, sulfide gases.
- It is a simple drive circuit